## Slide 1
AODV in MATLAB
CpE 6420 Project Presentations
Stuart Miller

## Slide 2
Background
Examples
Traffic Statistics
Future Work
Conclusions
Demo
FONTS

## Slide 3
AODV Routing Algorithm
Routing protocol for ad-hoc wireless networks
Outlined in RFC 3561
  C. Perkins, E. Belding-Royer, S. Das, "Ad hoc On-Demand Distance Vector (AODV) Routing", RFC 3561, July 2003. (https://www.rfc-editor.org/rfc/rfc3561.txt)
Utilized by Zigbee specification

## Slide 4
AODV Principles
Reactive routing protocol
Reduces network-wide broadcasts
Lower overhead
Discovers routes only as necessary
Relies on flooding for route discovery
Each node maintains its own route table

## Slide 5
AODV Route Messages
Route Request (RREQ)
  Sent when a node doesn’t have a valid path to the destination, triggers flooding
Route Reply (RREPL)
  Sent back to source when the destination is reached or an intermediate node has a route to the destination.
Route Error (RERR)
  Send back up the path of propagation by a node when its link to the intended destination breaks
Data
  Just normal packets containing actual information

## Slide 6
Approach
Implement in MATLAB, make use of high-quality GUI environment
Focus on resiliency throughout node movement (broken links, etc.)
Serve as more of a demonstration tool rather than an in-depth simulation
Focus on showing step-by-step progress of algorithm

## Slide 7
Background
Examples
Traffic Statistics
Future Work
Conclusions
Demo
FONTS

## Slide 8
Example 1
  Sending node D -> G
  All routing tables start empty
D floods with RREQ
G replies with RREPL
Data sent once route established
Subsequent transmissions require no new overhead

## Slide 9
Example 1
Reverse routes set up during flooding
Forward route set up during reply

## Slide 10
Example 2
  Sending node C -> G
  Intermediates nodes have route info from Ex. 1
C floods with RREQ
D,A,&G all reply with RREPL
C picks reply with smallest hop count to destination
Data sent once route established

## Slide 11
Example 2
More routes added

## Slide 12
Example 3
  Sending node D -> G again
  Node E has been moved, breaking links
D tries sending normally
A can’t reach E anymore, so replies with RERR
A now knows no routes, so must flood
C knows a route to G so replies
D sends to G

## Slide 13
Example 3
The RERR canceled out A->G
The sequence numbers changed

## Slide 14
Example 4
  Much shuffling, routes have almost all changed
Multiple route cancellations
Once C receives a reply, it sends out data, to the node with the lowest hop count to destination, expecting it to make it
Floods multiple times
D’s route to F is still valid though

## Slide 15
Example 4

## Slide 16
Background
Examples
Traffic Statistics
Future Work
Conclusions
Demo
FONTS

## Slide 17
Static Network
500 random packets sent
No movement, nodes remain in the same place
No RERRs

## Slide 18
Static Network
No movement
Propagation delays

## Slide 19
Mobile Network
500 random packets sent
Movement every 50 packets

## Slide 20
Static Network
Movement every 50 packets
Propagation delays

## Slide 21
Highly Mobile Network
500 random packets sent
Movement every 5 packets sent

## Slide 22
Static Network
Movement every 50 packets sent
Propagation delays

## Slide 23
One-Dimensional Network
500 random packets sent
Movement every 5 packets sent
Nodes only move in the X direction

## Slide 24
One-Dimensional Network
Two-Dimensional Network
One-Dimensional Network

## Slide 25
Background
Examples
Traffic Statistics
Future Work
Conclusions
Demo
FONTS

## Slide 26
Future Work
Compare to other protocol like DSDV or DSR
Implement other sources of delay such as queuing

## Slide 27
Background
Examples
Traffic Statistics
Future Work
Conclusions
Demo
FONTS

## Slide 28
Conclusions
Highly congested networks are a burden for any protocol
AODV handles link breakage with minimal overhead in simplistic cases
Works best when there aren’t multiple routes to choose or cancel out

## Slide 29
Background
Examples
Traffic Statistics
Future Work
Conclusions
Demo
FONTS

## Slide 30
Demo

## Slide 31
Questions?